|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 Thirteenth Regional Conference |  |
| --- | --- | --- |

August 7 - 11, 2006	Bangalore, India

Document No. 06/XIII/027

Agenda Item: 11.5

New Zealand Band Plans – Update

A Paper from the New Zealand Association of Radio Transmitters Incorporated (NZART)
for Presentation at the 13th IARU Region 3 Conference Bangalore, India, August 2006

Introduction

This document tables a copy of the current band plans in effect in New Zealand, as at May 2006.  These band plans are attached in the following pages.

New Zealand amateurs have access to all the traditional MF, HF, VHF, UHF and SHF bands.

We also have access to a band at 1800 metres (130 – 190 kHz), access on a “secondary” basis to 7.1 – 7.3 MHz on 40 metres (since 1978), and an 11 metre telemetry allocation.  A 50 cm band (614 – 622 MHz, UHF TV channel E39), is principally used for an ATV output channel.  Only limited access is permitted to the 50 –51 MHz part of the 6 metre band (special permit by geographical areas/TV Channel 1 coverage areas).

Key Changes

Key changes over the last 3-year period have been:

- With further changes to a single class of licence for all amateurs, all references to classes of license have now been deleted (N, G and T).  (Sub-bands for Novice operators (in the 80 m, 15 m, 11 m, 10 m and 2 m bands) had been previously removed).

- 1800 metre Band – extended down to 130 kHz

- 11 metre Telemetry Band limits changed to 26.950 – 27.300 MHz

- 32 cm Band limits changed to 921.000 – 929.000 MHz

Recommendation

That:

Region 3 Societies note the NZART Band Plans, and the changes that have occurred over the last 3 years

## NEW ZEALAND AMATEUR RADIO BAND PLANS

## These charts show the New Zealand bandplans.

These bandplans are to ensure that your transmissions do not impose problems on other operators and that their transmissions do not impact on you.

It is to the advantage of all operators that the published bandplans be used.

The Ministry of Economic Development (MED) defines the band limits, while the internal band segments are derived from the IARU Region 3 bandplans with New Zealand adaptations.

The band limits are found in "Schedule 3" (attached to each amateur radio licence) and on the NZART web site in the Study Guide (Regulations). (see note 1 below for URL)

The Region 3 bandplans are at the IARU Region 3 web site. (see note 2 below for URL)

| 0.130 |  | 0.190 |
| --- | --- | --- |

| 1.800 |  | 1.840 |  | 1.950 |
| --- | --- | --- | --- | --- |

| 3.500 |  | 3.550 | 3.620 |  | 3.640 | 3.900 |
| --- | --- | --- | --- | --- | --- | --- |

| 7.000 | 7.030 | 7.040 |  | 7.100 | 7.300 |
| --- | --- | --- | --- | --- | --- |

| 10.100 |  | 10.140 | 10.150 |
| --- | --- | --- | --- |

Note 1: NZART web site:

http://www.nzart.org.nz/nzart/exam/

Note 2: IARU Region 3 web site:

http://www.jarl.or.jp/iaru-r3/r3bandplan.doc

| 14.000 |  | 14.070 | 14.112 |  | 14.350 |
| --- | --- | --- | --- | --- | --- |

| 18.068 |  | 18.100 | 18.110 |  | 18.168 |
| --- | --- | --- | --- | --- | --- |

| 21.000 | 21.070 | 21.125 | 21.450 |
| --- | --- | --- | --- |

| 24.890 |  | 24.920 | 24.930 |  | 24.990 |
| --- | --- | --- | --- | --- | --- |

KEYS

= CW or modes less than 1 kHz bandwidth

= All modes with bandwidth less than 6 kHz

= Data/packet, less than 6 kHz bandwidth

Prepared by Jamie Pye ZL2NN May 2006

Updates or Comment to: zl2nn@nzart.org.nz

For the latest listings see:

http://www.nzart.org.nz/nzart/Repeaters/

| 26.950 |  | 27.300 |
| --- | --- | --- |
| Also designated for Industrial, Scientific and Medical purposes |

| 28.000 | 28.050 | 28.150 | 29.500 | 29.600 | 29.700 |
| --- | --- | --- | --- | --- | --- |

| 50.000 | 50.100 | 51.000 | 52.600 | 53.000 | 53.600 | 54.000 |
| --- | --- | --- | --- | --- | --- | --- |

Refer to the 'Additional Note' indexed in the Regulations part of the Study Guide on the NZART web page (see Note 1 at the bottom of page 1, of these bandplans, for the Internet address)

| 144.000 | 144.100 | 144.250 | 144.300 | 144.575 | 144.700 | 145.200 | 145.300 | 145.800 | 146.000 | 146.4125 | 146.600 | 147.0125 | 147.3875 | 147.6125 | 148.000 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | B |  | P |  |  |  | S |  | FM |  |  | FM |  |

| 430.000 | 431.000 | 432.250 | 432.300 | 433.000 | 435.000 | 438.000 | 440.000 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| L |  | B |  |  | S |  |
| ATV |

KEYS

= Repeater input band segment

= Repeater output band segment

= CW or modes less than 1 kHz bandwidth

= All modes

= Data/packet, less than 6 kHz bandwidth

= Repeater outputs only

ATV = Amateur Television, S = Satellites,
B = Beacons, P = Packet, FM = FM simplex,
L = Link

| 614.000 |  | 622.000 |
| --- | --- | --- |
| ATV |

| 921.000 | 921.200 | 925.250 | 925.300 | 928.800 | 929.000 |
| --- | --- | --- | --- | --- | --- |
|  |  | B |  |  |
| Also designated for Industrial, Scientific and Medical |

To find the narrow band segment bandplan for the microwave bands, please look for Simplex and Calling Frequencies that can be found elsewhere in this Call Book

Prepared by Jamie Pye ZL2NN May 2006

Updates or Comment to: zl2nn@nzart.org.nz

For the latest listings see:

http://www.nzart.org.nz/nzart/Repeaters/

| 1240 | 1256 | 1258 | 1260 | 1270 | 1274 | 1290 | 1294 | 1296 | 1297 | 1298 | 1300 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ATV |  | L | S |  | ATV |  |  |  |  | L |

| 2396 | 2400 | 2405 | 2407 | 2423 | 2424 | 2425 | 2427 | 2429 | 2445 | 2446 | 2450 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L | S |  | ATV |  |  |  |  | ATV |  | L |
| Also designated for Industrial, Scientific and Medical (ISM) purposes |

| 3300 | 3355 | 3359 | 3395 | 3399 | 3400 | 3410 |
| --- | --- | --- | --- | --- | --- | --- |
| ATV |  | ATV |  |  | S |

| 5650 | 5670 | 5760 | 5761 | 5830 | 5850 |
| --- | --- | --- | --- | --- | --- |
| S |  |  |  | S |

| 10 000 | 10 368 | 10 369 | 10 450 | 10 500 |
| --- | --- | --- | --- | --- |
|  |  |  | S |

| 24 000 | 24 050 | 24 192 | 24 193 | 24 250 |
| --- | --- | --- | --- | --- |
| S |  |  |  |

| 47 000 | 47 088 | 47 089 | 47 200 |
| --- | --- | --- | --- |

| 75 500 | 80 640 | 80 641 | 81 000 |
| --- | --- | --- | --- |

KEYS

= Repeater input band segment

= Repeater output band segment

= All modes

= Standard 1 MHz narrow band segment

ATV = Amateur Television, S = Satellites,
L = Link

NOTE: Plans are in development for bands above 122.25 GHz

To find the narrow band segment bandplan for the microwave bands, please see the list of Simplex and Calling Frequencies on the following page.

Prepared by Jamie Pye ZL2NN May 2006

Updates or Comment to: zl2nn@nzart.org.nz

For the latest listings see:

http://www.nzart.org.nz/nzart/Repeaters/

NEW ZEALAND SIMPLEX AND CALLING FREQUENCIES

144.100 MHz	Oceania SSB Calling

144.200	NZ SSB Calling

144.500	FM Calling

144.575	Data Simplex and APRS

144.600	Primary Data/Packet port - linked to Digital National System

144.625	Secondary Data/Packet port - linked to Digital National System

144.650	Primary Local Data/Packet Store/Forward

144.675	Secondary Local Data/Packet Store/Forward

145.250	Narrow band picture modes: FAX, Hellschreiber, SSTV etc.

146.425 to 146.600	FM SIMPLEX

  - FM Calling

147.400 to 147.600	FM SIMPLEX

147.500	Tertiary Local Data/Packet Store/Forward

432.200 MHz	SSB Calling

432.500	FM Calling

432.575	Data Simplex and APRS

432.600	Primary Data/Packet port - linked to Digital National System

432.625	Secondary Data/Packet port - linked to Digital National System

432.650	Primary Local Data/Packet Store/Forward

  - Secondary Local Data/Packet Store/Forward

438.700	Voice-over-Internet Simplex

438.300	Tertiary Local Data/Packet Store/Forward

Above 144 MHz, use the following as a guide to designated frequencies:

F to F+1.000 MHz for standard narrow band or weak signal segment, where

F = 144, 432, 621, 925, 1296, 2424, 3399, 5760, 10368, 24192, 47088, 80640 MHz.

F+0.200 kHz SSB calling

F+0.250 kHz to 0.300 kHz Beacons (Geographic plan, 1 kHz spacing)

F+0.500 kHz FM calling

F+0.575 kHz Data Simplex and APRS

F+0.600 kHz Primary data/packet port - linked to National System

F+0.625 kHz Secondary data/packet port - linked to National System

F+0.650 kHz Primary local data/packet

F+0.675 kHz Secondary local data/packet

F+0.700 kHz Voice-over-Internet Simplex

There may be additional designated frequencies in this segment in some bands.

Prepared by FMTAG 2005

# Text boxes

130 to 190 kHz – 1800 metres

Radiated power must not exceed 5 watts e.i.r.p.

1.800 to 1.950 MHz – 160 metres

3.500 to 3.900 MHz – 80 metres

7.000 to 7.300 MHz – 40 metres

Amateur satellite service permitted 7.0-7.1 MHz

7.1 to 7.3 MHz access is secondary to other users

10.100 to 10.150 MHz – 30 metres

14.000 to 14.350 MHz – 20 metres

Amateur satellite service permitted 14.00-14.25 MHz

18.068 to 18.168 MHz – 17 metres

Amateur satellite service permitted in whole band

21.000 to 21.450 MHz – 15 metres

Amateur satellite service permitted in whole band

24.890 to 24.990 MHz – 12 metres

Amateur satellite service permitted in whole band

12/06/2006 7:24:57 p.m.

26.950 to 27.300 MHz – 11 metres

Telemetry or telecontrol only, 5 W e.i.r.p. maximum

28.000 to 29.700 MHz – 10 metres

Amateur satellite service permitted in whole band

51.000 to 53.000 MHz – 6 metres

SSB/CW calling 52.05 MHz, FM calling 52.525 MHz. 53.6-54 MHz available for MED approved fixed transmitters

Repeater Outputs Only

MED permitted operation only
 50-51 MHz*

144.000 to 148.000 MHz – 2 metres

Amateur satellite service permitted in the range 144-146 MHz. Oceania SSB calling 144.1 MHz, ZL calling 144.2 MHz, FM calling 144.5 and 146.475 MHz. Primary packet/digipeater 144.65 MHz, other frequencies available. Below 147 MHz, repeater offset -600 kHz, otherwise +600 kHz; Beacons 144.250 - 144.300 MHz.

430.000 to 440.000 MHz – 70 cm

Amateur satellite permitted in the range 435-438 MHz. SSB calling 432.2 MHz, FM calling 432.5 MHz, Beacons 432.25-432.30 MHz. Primary packet/digipeater 432.65 MHz, other frequencies available. Repeater offsets -5 MHz in most cases, +5 MHz otherwise. In general, the ATV repeaters have an input frequency of 431.250 MHz vision, 436.750 MHz FM sound and 437.100 MHz NICAM sound

614.000 to 622.000 MHz – 50 cm

ATV vision carrier 615.25 MHz ITU(R) system G

921.000 to 929.000 MHz – 32 cm

Power 25 W e.i.r.p., SSB calling 925.2 MHz, FM calling 925.5 MHz. Beacons 925.25-925.30 MHz

12/06/2006 7:24:57 p.m.

1240 to 1300 MHz – 23 cm

SSB calling 1296.2 MHz, FM calling 1296.5 MHz. Beacons 1296.25-1296.30 MHz. ATV video carriers 1241.25, 1249.25, 1275.25 and 1283.25 MHz ITU(R) system G. Repeaters -20 MHz offset. Amateur satellite service in band 1260- 1270 MHz, uplink only

2396 to 2450 MHz – 12 cm

Standard 1 MHz narrow band segment 2424-2425 MHz. SSB calling 2424.2 MHz, FM calling 2424.5 MHz. Beacons 2424.25-2424.30 MHz. ATV in segments 2408-2422 and 2432-2446 MHz, ITU(R) system B. Repeaters -20 MHz offset. Amateur satellite service in 2400-2450 MHz. 2400-2450 MHz is also designated for Industrial, Scientific and Medical (ISM) purposes

3300 to 3410 MHz – 9 cm

5650 to 5850 MHz – 5 cm

Satellites 5650-5670 MHz earth-to-space only; 5830-5850 MHz space-to-earth only

10 000 to 10 500 MHz – 3 cm

24 000 to 24 250 MHz – 1.2 cm

47 000 to 47 200 MHz – 6 mm

Amateur satellite available on the entire band

75 500 to 81 000 MHz – 4 mm

Amateur satellite available on the entire band

12/06/2006 7:24:57 p.m.