|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 Thirteenth Regional Conference |  |
| --- | --- | --- |

August 7 - 11, 2006	Bangalore, India

Document No. 06/XIII/044

Agenda Item: 11.5

Wireless Institute of Australia

NEW AUSTRALIAN 7 MHz BAND PLAN

The Wireless Institute of Australia has developed and proposed a new Australian band plan for the 40m (7 MHz) amateur band.

The new plan is designed to

- encourage activity above 7100 kHz;

- stimulate experimentation in wideband digital modes; and

- integrate, as far as is possible, with the IARU region 3 plan, and the plans of other countries.

The underpinning philosophy of the plan is to define band usage in terms of necessary bandwidth, rather than by mode.

However, it is recognised that some modes are incompatible, such as analogue voice and data.  Accordingly, these modes are each assigned their own sections in the plan.

Features of the new plan include:

- To better provide for the WIA weekly Sunday broadcast that is currently transmitted on various frequencies from different call areas and time zones, a new broadcast segment from 7130-7150 kHz has been chosen.

- A new wideband data modes segment from 7180-7250 kHz, which is further sub divided into unattended/automated and attended segments.  The subdivision serves to prevent interference between automated and non-automated data stations.

- Redefinition of the CW segment (7-7030 kHz) to a narrow band modes segment with a maximum necessary bandwidth of 200 Hz.  This means, in effect, that the previously exclusive CW segment will be shared with PSK31 and other very narrow band data modes.

The change to the previously exclusive CW segment is in accordance with evolving international practice.  It is worth noting that the ZL 40m band plan has had a CW/PSK sharing arrangement in place for some time.  Moreover, CW/PSK sharing is proposed under the new US 40m band plan.

The new 40m band plan is detailed as follows:

| Segment (kHz) | Use |
| --- | --- |
| 7000-7030 | Very narrow band modes (maximum necessary b/w 200 Hz) |
| 7030-7040 | Narrow band digital (maximum necessary b/w 2 kHz) |
| 7040-7180 | Analogue telephony (maximum necessary b/w 8 kHz as per the amateur licence conditions) |
| 7130-7150 | Broadcast sub-segment |
| 7180-7190 | Wideband digital, unattended (maximum necessary b/w 8 kHz as per the amateur licence conditions) |
| 7190-7250 | Wideband digital (maximum necessary b/w 8 kHz as per the amateur licence conditions) |
| 7250-7300 | Analogue telephony (maximum necessary b/w 8 kHz as per the amateur licence conditions) |

Obviously, the current levels of broadcast station interference above 7100 kHz will mean that some degree of flexibility is required in use of the new band plan.

Australian amateurs currently have access to 7100-7300 kHz on a secondary basis.  The plan is designed to be fully implemented once 7100-7200 kHz reverts to amateur primary use in 2009.

____________________