|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 B A N D P L A N |  |
| --- | --- | --- |

135 KHz

1.8 MHz

3.5 MHz

Note :

- Where the total band available nationally is 100 kHz or less, phone operation
may commence at 3.525 MHz.

- Emergency CoA frequency 3.600 MHz ( All Modes ± 5 KHz )

7 MHz

Co primary

Note : Emergency CoA frequency 7.110 MHz ( All Modes ± 5 KHz )

10 MHz

14 MHz

Note:

- Considering the dramatic increase in data mode usage on the 20 meter band, it is recommended that the sub-band for these classes of signals be 14.070 MHz to 14.112 MHz (with +/- 500 Hz at 14.100 MHz for beacons), and within that data sub-band the current practices of traditional data modes may continue up to 14.095 MHz with 14.095 to 14.112 MHz being reserved for other data modes including Packet.

- Emergency CoA frequency 14.300 MHz ( All Modes ± 5 KHz )

18 MHz

Note : Emergency CoA frequency 18.160 MHz ( All Modes ± 5 KHz )

21 MHz

Note : Emergency CoA frequency 21.360 MHz ( All Modes ± 5 KHz )

24 MHz

28 MHz

50 MHz

144 MHz

430 MHz

1,240 MHz

Bands above 1300 MHz:

Societies should consult with the amateur satellite community for proposed satellite operating frequencies before deciding local bandplans above 1300 MHz.

The Basic Principles Underlying the IARU Region 3 Bandplan:

(1) In all cases of conflict between a bandplan and the national regulations of a country, the latter shall prevail.

(2) Nothing in these bandplans shall be construed as prohibiting different national arrangements, provided that harmful interference is not caused to stations in countries operating in accordance with the regional bandplan.

(3) Notwithstanding item 2 above, Member Societies of IARU Region 3 are strongly urged to use these regional bandplans as a basis for their national bandplans.

[Legends]

CoA:	Emergency Centre of Activity frequency

EME:	Earth-Moon-Earth, Meteor Scatter, Auroral Scatter and other weak-signal

NB:	Narrow band modes including CW, RTTY, Packet and modes with similar bandwidth not exceeding 2 kHz.

Phone:	Phone operation includes SSTV, FAX and modes with similar bandwidth not exceeding 6 kHz.

Satellite:	This segment should be kept clear of other operating modes.

Secondary:	At 7.2 to 7.3 MHz, amateur stations shall not cause harmful interference to stations of the Broadcasting Service.

WB:	Wide band modes including FM.

Adopted at the IARU R3 15th conference, Ho Chi Minh City, Viet Nam 2012

____________________

# Text boxes

1,240

EME

1,297

1,296

Satellite

1,270

1,260

450

431.9

435

432.240

438

EME

Satellite

430

Secondary

145.8

146

148

144

144.035

EME

Satellite

50

54

50.1

50.5

Phone and NB

WB

Beacons

CW

28.2

International
Beacon
( 500 Hz
guard band
for beacons

28.0

29.510

28.68 ( 5 kHz
is recommended
for SSTV

29.3

28.050

28.150

28.3

28.190

WB

Satellite

NB

Phone Operation

Beacons

CW

29.7

NB

CW

24.89

Phone

21.360

CoA

21.15

International Becon

( 500 Hz
guard band
for beacons

21.12540

21.070

21.34

( 5 kHz
is recommended
for SSTV

Phone Operation

CW

21.45

21.0

NB

18.110

International Beacon
( 500 Hz
guard band
for beacons

18.160

CoA

18.068

18.168

18.100

NB

Phone

CW

24.930

International Beacon
( 500 Hz
guard band
for beacons

14.23

( 5 kHz
is recommended
for SSTV

14.1127.040

14.070

NB

NB

Phone Operation

CW

14.0

10.10

10.157.3

Secondary

NB

10.14

CW

7.0

CW

7.3

7.030

7.025

7.040

7.1

Secondary

7.2

7.110

CoA

NB

NB

Phone Operation

3.600

CoA

Phone Operation

CW

3.5

3.9

3.510

RTTY

DX

1.840

1.8

2.0

1.830

1.834

Phone Operation

CW

135.7 KHz

137.8 KHz

Phone

DX

3.535

3.800

3.775

Secondary

CW / NB

CW

DX

14.35

14.300

CoA

14.1

International Beacon

( 500 Hz
guard band
for beacons

24.99

24.920

1,3000

Revised: 8 November 2012

CW & NB

Secondary

472 kHz

479 kHz